## Slide 1: SmallFlow - 080000 Overview

## Slide 2: SmallFlow - 080000
Product Overview

## Slide 3: SmallFlow – 080000 Technical
Compact
Micro Cv
Flexible
Different bonnet types
Ideal for laboratories and pilot plants

## Slide 4: SmallFlow - 080000 Technical
screwed seat
Micro Cv
Plug head guided
Screwed bonnet
Safety packing
Size | ¼ inch
Pressure Class | CL 2500 / PN400
Body Materials | 1.4571 Other materials upon request
Body Type | Globe, Angle
End Connections | ¼“ NPT, G ¼“
Cv range | 0.000063 – 0.29
Trim Type | Parabolic low flow
Specials | Very low Cv control
Microflow applications with very low Cv requirements. Reproducible equal percentage characteristic. Chemical injection applications. Small scale plants. Pilot plants.
Large stroke (10mm) for better control.

## Slide 5: SmallFlow – 080000 Actuator Options
Pneumatic P1
  Fail open / Fail close
  Multispring
  Optional Positioner
  Yoke or yoke rod design
Electric E1
  24V AC / 230V AC
  Self calibrating
  Positioner integrated

## Slide 6: SmallFlow - 080000 Trim Design
Annular gap
Flat throttling
Notch throttling

## Slide 7: Thank You
SmallFlow-080000 Overview R00.pptx 14.12.2018 SG